NK2-22

Heavy duty high head pumps capable of handling abrasive materials with minimal wear

Heavy duty, high head single-phase pumps available in 220v. Optional agitator kits allow continuous duty when pumping abrasive materials.

FEATURES

            - Semi Vortex Impeller and Synthetic Rubber Wear Plates for maximum durability and maintaining pump performance

            - Double inside Mechanical Seal with SiC faces provides the longest operational life

            - High head pump for maximum discharge distances

            - Oil filter provides lubrication of the seal faces (patent pending)

            - Built in thermal sensors to prevent motor failure

            - V-Ring seal design protects mechanical seal from abrasive particles

            - Maximum Capacity 130GPM

            - Available in 220V

Optional accessories

            - TS-303 Float Switch for automatic operation

            - Sand Kit to suspend solids and prevent clogging.

            - 2-inch NPT coupling available

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100

| Model | NK2-22 |
| --- | --- |
| Max. Capacity (GPM) | 130 |
| Max. Head (ft) | 85 |
| Discharge Connection (in) | 3” |
| Motor Output | 3hp |
| Voltage (V) | 220V |
| Amperage – rated current | 13 |
| Amperage – starting current | 70 |
| Std. Cable length (ft) | 32 |
| Max. Cable Length (ft) | 94 |
| Min. Generator Capacity (watts) | 8000 |
| Max. Diameter (in.) | 9 7/16 |
| Max. Height (in.) | 24 ½ |
| Continuous Running water level (in.) | 3 ¼ |
| Pump Weight | 81 lbs |

# Sand Kit

Turn your NK Series dewatering pump into a sand/aggregate pump with the addition of our sand kit to your order. Our sand kit helps suspend the sand and solids that you sometimes encounter on what should have been a routine dewatering application.

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100