LB-480-62

Powerful pumps built with durable materials in an easy handling design.

Top discharge provides maximum motor cooling efficiency allowing continuous duty operation at low water levels and extended dry-run capability

FEATURES

            - Urethane, Semi Vortex Impeller and Wear Plates for maximum durability and maintaining pump performance.

            - Double Inside Mechanical Seal With SiC faces provides

the longest operational life.

            - Oil Lifter provides lubrication of the seal faces. (patent pending)

            - V-Ring Seal design protects mechanical seal from abrasive     particles

Optional accessories

            - TS-301 Float Switch for automatic operation

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100

| Model | LB-480-62 |
| --- | --- |
| Max. Capacity (GPM) | 62.4 |
| Max. Head (ft) | 39.5 |
| Discharge Connection (in) | 2” |
| Motor Output | 2/3 hp |
| Voltage (V) | 110V |
| Amperage – rated current | 6.1 |
| Amperage – starting current | 12.5 |
| Std. Cable length (ft) | 32’ |
| Max. Cable Length (ft) | 62’ |
| Min. Generator Capacity (watts) | 1300 |
| Max. Diameter (in.) | 7 3/8 |
| Max. Height (in.) | 11 3/16 |
| Continuous Running water level (in.) | 2” |
| Pump Weight | 28 lbs |

| Tether length | Pumping range |
| --- | --- |
| 3.5 (in) | 7 (in) |
| 6 (in) | 10 (in) |
| 10 (in) | 16 (in) |
| 14 (in) | 22 (in) |
| 18 (in) | 28 (in) |
| 22 (in) | 33 (in) |
| 24 (in) | 36 (in) |
| Note: Due to weight of cable, pumping range above horizontal is NOT equal to pumping range below horizontal. As tether length increases, so does the variance of the pumping range. Pumping ranges are based on testing in non-turbulent conditions. Actual conditions may vary. |

Float Switch Range

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100